## Slide 1: ASTRO CATS
Preliminary Design Review Presentation
Notes: Aaron

## Slide 2: Team
Nicholas Fagan – Team Lead
Brandon Horne – Payload Lead
Kevin Eliason – Rocket Lead
Aaron Deutsch – Safety Lead
Andrew Auffenberg
Caleb Wasmund
Justin Malloney
Cameron Crippa
Gabriel Punte-Lay
Jake Chesley
Notes: Aaron

## Slide 3: Presentation Outline
Project Statement
Project Budget, Schedule and Objectives.
Vehicle dimensions, materials, and justifications
Static Stability Margin
Plan for vehicle safety verification and testing
Baseline motor selection and justification
Thrust-to-weight ratio and exit rail velocity
Launch vehicle verification and test plan overview
Drawing/Discussion of each component and subsystem
Baseline Payload Design
Payload verification and test plan overview
Upcoming Team Events
Notes: Aaron

## Slide 4: Project Statement
The Astro Cats will win the NASA University Student Launch by developing a vehicle capable of deploying a planetary probe to approximately 1 mile above ground level. The probe will be deployed via a custom fairing system and will capture atmospheric data. The data will then be transmitted via radio to a ground station. This system will be developed for under $7,500.
Notes: Aaron

## Slide 5: Level 1 Safety Analysis
Please be aware of any hazards that exist in the room
  Tripping hazards – cords, chair legs, and backpacks
  Pinch points – hands with doors and hands in between chairs and desks
In the event that we need to evacuate please exit the building out the main entrance and meet in quad.
In the event that we need to shelter in place please make your way to the 400 level of Baldwin and shelter in the hallway.
Notes: Aaron

## Slide 6: Work Breakdown Structure
Notes: Aaron

## Slide 7: Project Budget
Started purchasing components Oct 14th
Currently under initial proposed budget by $991
Notes: Nick

## Slide 8: Project Funding
Already secured funds from UC SEDS & Aero department
Plan to present project presentation to companies requesting funds in December
In the process of completing OSGC Grant
Notes: Nick

## Slide 9
Notes: Nick

## Slide 10
Notes: Nick

## Slide 11: Launch Vehicle Objectives
Vehicle shall deliver the payload to as close to 5,280 ft (AGL) as possible.
Vehicle shall be reusable after recovery.
Tracking bay shall transmit position data back to ground station.
At landing, each independent section of the launch vehicle shall have a maximum kinetic energy of 75 ft-lbf.
Vehicle will deploy parachutes via stratologger altimeters
Notes: Nick

## Slide 12: Payload Objectives
The payload shall deploy at apogee
The payload shall collect atmospheric measurements
The payload shall take pictures
The payload shall remain in orientation during descent and after landing
The data from the payload shall be stored onboard and transmitted wirelessly to the ground station
The payload will be reusable after the mission
Notes: Nick

## Slide 13: Launch Vehicle Overview
Design Overview
Fairing Design
Fin Design
Motor Selection
Tracking Bay Design
Integration
Mass Breakdown
Notes: Nick

## Slide 14: Launch Vehicle Design
Total length: 84.4 inches
Airframe Diameter: 5.54”
Fin count: 3
Empty weight: ~12 lbs
Loaded weight: ~19 lbs
Center of Gravity: 46.79”
Center of Pressure: 57.99”
Stability Margin: 2.04
Number of Subsections: 4
Notes: Kevin

## Slide 15: Fairing Design
Mold made from standard 5.54” plastic nosecone
Layers of 4 oz. and 6 oz. fiberglass and epoxy resin
Interlocking machined polymer rib structure
Overlapping tab to reduce airflow leakage
Nylon shear screws to join pieces
Tethered to P.I.L. parachute
Notes: Kevin

## Slide 16: Fin Design
Fin Count: 3
1/16” G-10 Fiberglass plastic core
5lb. Divinycell foam shaped to airfoil
6oz. Fiberglass and epoxy shell
Permanently attached to lower body tube
Notes: Kevin

## Slide 17: Motor Selection
Motor: Cesaroni – P54-5G Classic (K570)
Size: 54 mm
Burn time: 3.6 sec
Total Impulse: 2062.9 Newton-Seconds
Max Thrust: 892.7 Newtons
Mass: 1685.0 grams
Delay charge will be removed
Notes: Kevin

## Slide 18: Tracking Bay
Components:
  Arduino Mega
  XTEND-900 radio transceiver
  Venus GPS Module
  Radio and GPS Antenna
  Battery
Communicates vehicle position data back to ground station in real time.
Notes: Jake

## Slide 19: Tracking Bay Electronic Schematic
Notes: Jake

## Slide 20: Integration
2 separation points – fairing and below recovery bay
P.I.L. housed in fairing
Drogue chute in upper section beneath the P.I.L.
Main chute in lower section between Recovery and tracking bays
Notes: Gabe

## Slide 21: Mass Breakdown
Subsection | kilograms | lbs
Total Lower Section Mass | 3.61 | 7.97
Total Upper Section Mass | 1.14 | 2.51
Total Recovery Bay Mass | 1.13 | 2.48
Total Tracking Bay Mass | 0.94 | 2.06
Total P.I.L. Mass | 1.52 | 3.34
Total Mass |  | 18.36
Lower Section
Upper Section
Recovery Bay
Tracking Bay
P.I.L.
Notes: Gabe

## Slide 22: Static Stability Margin
 | On Launch Pad | After Burnout
CP (from tip) | 57.99 in. | ---
CG (from tip) | 46.79 in. | 43.15 in.
Static Margin | 2.04 | 2.70
Notes: Gabe

## Slide 23: Motor Selection, thrust-to-weight ratio, exit rail velocity
Currently we are using a Cesaroni K570 which has a total impulse of 2070.258 N-Sec and a 3.9 sec. burn time
  Preliminary test show a total altitude of 5,740.30 feet.
  Thrust-to-Weight Ratio: 6.77
  Max velocity: 659.24 feet/second
  Exit rail velocity: 64.22 feet/second
Also considering using a Cesaroni K750-RL which has a total impulse of 2361.966 N-Sec and a 3.14 sec. burn time
  Preliminary test show a total altitude of 6,638.85 feet.
  Thrust-to-Weight Ratio of 8.53
  Max velocity of 765 feet/second
  Exit rail velocity: 41.4223 feet/second
Notes: Gabe

## Slide 24: Launch Vehicle Testing Plan
  Launch Vehicle
    Subscale launch
    Wind tunnel
    Parachute drop tests
    Full scale launch– simulated payload
    Full scale launch – full integration
  Fairing
    Pop tests
    Impact and vibration testing
  Electronics
    Radio communication tests
    Altimeter vacuum test
Notes: Gabe

## Slide 25: Parachute Summary
Section | Surface Area (ft2) | Drag Coefficient | Descent Rate (ft/sec) | Kinetic Energy at impact (ft-lbf)
Main Parachute | 57 | 1.26 | 14.2 | 35.3
Drogue Parachute | 7.1 | 0.75 | 46 | -
PIL Parachute | 12.6 | 0.75 | 22.5 | 44.6
Notes: Caleb

## Slide 26: Recovery Systems
Parachute Summary
PIL Recovery System
Rocket Recovery System
Ejection Charges
Attachment Method & Durability
Notes: Caleb

## Slide 27: PIL Recovery System
The PIL recovery will be a single parachute.
The PIL will deploy its parachute at apogee.
  PIL Parachute: Public Missiles PAR-60HD
  Descent rate is approximately 22.5 (ft/sec)
    Current mass calculation: 5.7 lbs.
Notes: Caleb

## Slide 28: Rocket Recovery System
The rocket will be a two stage deployment after releasing the PIL.
A drogue parachute will deploy five seconds after apogee.
  Drogue Parachute: 36” LOC LHPC-36
  Slows descent rate to approximately 46 (ft/sec)
    Current mass calculations: 11.3 lbs.
A main parachute will deploy at 600 feet (AGL).
  Main Parachute: SkyAngle CERT-3 Large
  Slows the rocket to an approximate final descent rate of 14.2 (ft/s)
    Current mass calculations: 13.4 lbs.
Notes: Caleb

## Slide 29: Ejection Charges
Two black powder charges will be used for both the drogue and main parachute.
Each parachute deployment will have a 1.5 gram main charge and a 2 gram redundant charge.
  Pop-tests will refine these values.
The Recovery Bay Sled will have three StratoLogger altimeters.
  Strat 1 – Deploys main charge for faring and main parachute
  Strat 2 – Deploys main charge for the drogue and back-up for main parachute
  Strat 3 – Deploys back-up drogue charge
Notes: Caleb

## Slide 30: Attachment Method & Durability
Attachment method for all parachutes will be the rip-stop nylon provided with each and additional nylon suspension supports.
Rip-stop cords will be attached via eyebolts imbedded into the bulkheads of the Recovery Bay.
The load capacity of each parachute is not exceeded per suppliers provided calculators.
Notes: Caleb

## Slide 31: Drift-Wind Speed
Assumptions
  Sustained wind speeds change with a normal distribution
  The standard deviation is 2 feet/sec
Next steps
  Research and gather experimental data either supporting the current wind behavior, or find data to model a more accurate distribution
Graph to the right shows the wind speed distribution at a mean of 5 MPH (7.33 feet/sec). This was done for 0,5,10,15, and 20 MPH.
Notes: Justin

## Slide 32: Drift-Single Run
Assumptions
  Apogee is always 5,280 feet
  Wind speed probability is a normal distribution
On the right is a single drift estimate at 5 MPH
  Payload descends at a constant rate.
  The rockets main parachute is deployed at 600 feet
Notes: Justin

## Slide 33: Drift-Multiple Runs
Assumptions
  1 Degree-of-Freedom system
  All assumptions stated above apply.
The graph on the right shows a distribution of total drift at 5 MPH for the rocket.
  This was done for both the rocket and the payload at 0, 5, 10, 15, 20 MPH
  Can help us accurately predict landing zones
Notes: Justin

## Slide 34: Drift Range
Wind Speed MPH | Rocket Drift Feet | Payload Drift Feet
0 | 0 | 0
5 | 1,049-1,095 | 1,733-1,791
10 | 2,123-2,169 | 3,498-3,557
15 | 3,195-3,241 | 5,260-5,320
20 | 4,268-4,313 | 7,024-7,083
Notes: Justin

## Slide 35: Science Value
Data taken will reinforce the scientific knowledge base
Create plots of variables vs altitude
  Use pressure sensor to find altitude
Will analyze plots using MATLAB and other software
  Look for points of interest and abnormalities
Compare to known atmospheric models
  Plot errors compared to our data
Camera data will be analyzed visually for points of interest
Notes: Justin

## Slide 36: Payload Design Overview
Planetary Investigation Lander (PIL) Structure
Landing Module
PIL Hardware
Ground Control
Integration
Mass Breakdown
Notes: Cameron

## Slide 37: PIL Structure
Polymer Tri-structure for mounting
Clear acrylic PIL housing
Parachute connections mounted directly to main structure
Aluminum Landing base plate
Notes: Cameron

## Slide 38: Landing Module
Torsion spring leg deployment
Servo-motor with triangle retaining plate
Notes: Cameron

## Slide 39: PIL Hardware
Arduino Mega 2650 – Microcontroller
XTEND 900 – 1 Watt 900 MHz radio
SparkFun Venus GPS – GPS Module
RHT03 – Temperature and Humidity sensor
  Two used with alternating polling.
BMP180 – Barometric sensor
ML8511 – UV Sensor
Notes: Jake

## Slide 40: PIL Hardware Continued
Apogee Instruments SP-215 – Pyranometer
  continuously outputting voltage relating to solar irradiance (W/m2).
ADXL345 – Accelerometer
LS-Y201-2MP - JPEG Color camera
SparkFun microSD Transflash
  microSD Breakout board to write data to microSD
  Backup data storage in case of radio failure
Notes: Jake

## Slide 41: PIL Electronic Schematic
Notes: Jake

## Slide 42: Ground Control Hardware
Arduino Mega 2650
  Microcontroller that interfaces the radio transceiver with the PC
  Sends incoming radio data from the PIL and Tracking Bay to the PC
  Sends outgoing commands to the radio, to transmit to the PIL
XTEND-900 - Radio transceiver
PC - A laptop used to interface with the Arduino
  Collect and display gathered data using custom software
Notes: Jake

## Slide 43: Ground Control Electronic Schematic
Notes: Jake

## Slide 44: Ground Control Software
Arduino will collect data from radio that has been received from PIL and Rocket Tracking Bay, and send it to the PC over serial connection.
PC will utilize custom software that retrieves serial data sent from the Arduino.
Data will be parsed and the user interface display will be updated in real time with new data.
wxWidgets C++ GUI Library being used for GUI.
Notes: Jake

## Slide 45: System Integration - PIL and landing module
Notes: Brandon

## Slide 46: System Integration - PIL & Ground Ops
Notes: Brandon

## Slide 47: System Integration - PIL & Rocket
PIL and Rocket integration
  Payload adapter sleeve
  PIL slides into Adapter Sleeve
  Fairing Slides over Adapter Sleeve
  Adapter Sleeve is fixed to rocket
Notes: Brandon

## Slide 48: PIL Mass Breakdown
Chart: Payload Mass Budget
| Structure | Landing Module | Electronics
 | 856 | 168 | 492
Notes: Brandon

## Slide 49: Payload Testing Plan
 | Design Features to meet Requirement | Verification
 | The system is designed to be undamaged after launch with an easily replaceable motor. | This will be verified through testing.
 | The PIL system consists of all sensors necessary to record the atmospheric measurements at altitude and on the ground. | This will be verified through testing.
 | The PIL system is designed in a way to collect and transmit data at the required rate and for the required time. | This will be verified through inspection and testing.
 | The PIL system is design to hang in orientation under parachute at altitude and contains landing legs to remain in orientation on the ground. | This will be verified through testing.
 | The PIL system consists of onboard radios to transmit wirelessly to a ground station throughout the flight. Any missed packets of data will be retransmitted before end of operations on the ground. | This will be verified through testing.
 | The rocket contains a fairing and deployment mechanism. | This will be verified through analysis and testing.
 | The fairing system is tethered to PIL system, offering tracking and safe recovery of the fairing system. | This will be verified through inspection and testing.
Notes: Brandon

## Slide 50: Educational Engagement
Completed on November 4 at Winton Woods High School
  200 high school students
Water Bottle Rocketry
Taught about thrust, stability, drag, and fin design
Feedback forms to be sent to high school this week
Documentation sent to NASA next week
Notes: Andy